## Slide 1: Western Engineering Competition (WEC) Presentation
David, Neelesh, Mila

## Slide 2
1. Side Crossbow (clothespin on the side)
2. Slingshot
3. Slingshot with channel to guide bullet
Design Process
1
2
3

## Slide 3: Modelling Final
Clothespin
Popsicle sticks
Straw Channels
Notches for rubber bands

## Slide 4: Final Design
Elevated and angled off the floor
Tape along the bullet channel to reduce friction
Clothespin release trigger
Popsicle sticks along the top and straws on side to prevent bullet from straying from path
Straw channels
Clothespin

## Slide 5: Using Materials
Straws: Made channels to guide bullet, ensuring proper trajectory
Clothespin: Used as a release mechanism for the rubber bands
Cardboard: Used as stand for projectile contraption
Rubber Band: Recoil of rubber band used to apply initial force to dart
1

## Slide 6: Optimizing Distance + Performance
Most optimal angle found through trial and error was ~30 degrees.
  Maximizes the horizontal distance travelled
Straws are placed to create a pathway to guide the dart and ensure accuracy
  Straws have a low coefficient of friction (0.17 to 0.42)
Tied two rubber bands together to launch the bullet
  Ensures contraption can be pulled back far enough
  Found that three rubber bands was too much force